Project Title  (as descriptive as possible)
Portable Impedance Tomography System
Ashton Johnson
CPE621 Advanced Embedded Systems
Electrical and Computer Engineering
The University of Alabama in Huntsville
e-mail: acj0008@uah.edu

---
The Need
Impedance as a Tool
- Complex Impedance Measurements provide insight on material composition.
  - More information can be observed using real and imaginary components.

---
Potential Applications
- Electromechanical Impedance Spectroscopy (EIP)
  - Characterization of coatings and metal corrosions.
- Electrical Bioimpedance Spectroscopy (EBIS) is a growing area of research.
  - Impedance pneumography- Respiration Rates
  - Continuous ECG measurements are subject to interference from motion artifacts.
  - Body composition measurements
  - Electrical Impedance Tomography – Using impedance to build a 2D/3D image of the material.

---
Analog Devices AD5933
- Low cost, impedance analyzer system on chip.
- Programmable output peak-to-peak excitation voltage to a maximum frequency of 100 kHz
- Programmable frequency sweep capability with serial I2C interface
- Frequency resolution of 27 bits (<0.1 Hz)
- Impedance measurement range from 1 kΩ to 10 MΩ
- Capable of measuring of 100 Ω to 1 kΩ with additional circuitry
- Phase measurement capability
- 2.7 V to 5.5 V power supply operation

---
AD5933 Block Diagram

---
AD5933 Shortcomings
- The AD9533 front-end is not design for bioimpedance use.
  - Voltage driven interface without regard to current.
    - IEC-60601 defined current limits for human body.
  - Receive side has VCC/2 bias, therefor placing DC voltage on user.
  - 4 electrode measurement setup was introduced by Seoane et al.
    - Never disclosed the actual V-to-I and I-to-V conversion.

---
Breniuc et al.
- Wearable Impedance Analyzer
  - “Wearable”
  - Self contained UI
  - No front end additions

---
Harder et al.
- Presented a solution to measure fluid changes, and fat mass.
  - Developed a reliable body interface to the AD5933
  - Bluetooth connectivity

---
Dimas et al.
- 64-electrode Electrical Impedance Tomography system
  - Analog multiplexing 64 electrode system
  - Does not utilize AD5933

---
Proposed approach
Proposed approach
- Portable Impedance Tomography
- Combine features of existing solutions
  - Multiple electrodes – 4 point
  - AD5933
  - Bluetooth connectivity

---
Logistics
- Milestones
  - Hardware
    - Platform Selection (19 SEP)
    - Schematic Design & Layout Complete (26 SEP)
      - AD5933
      - Analog Multiplexers
      - Power Domain
    - PCB Assembly Complete (10 OCT)
    - PCB Checkout Complete (24 OCT)

---
Logistics
- Milestones (cont)
  - Software Development
    - Iterative deliveries based on SCRUM development cycles.
      - Sensor Module firmware development
      - GNU/Linux application development
      - (opt) Android application development

---
Philosophies
- Use and contribute free, libre, open source whenever possible.
  - PCB design will utilize KiCad
    - Design components will be submitted to official repositories.
  - GCC software compilation
  - Design and all document to be hosted at GitHub.
    - https://github.com/ashtonchase/portable_impedance_tomography

---
References
- L. Breniuc, V. David, and C. G. Haba, “Wearable impedance analyzer based on AD5933,” in 2014 International Conference and Exposition on Electrical and Power Engineering (EPE), 2014, pp. 585–590.
- R. Harder, A. Diedrich, J. S. Whitfield, M. S. Buchowski, J. B. Pietsch, and F. J. Baudenbacher, “Smart Multi-Frequency Bioelectrical Impedance Spectrometer for BIA and BIVA Applications,” IEEE Transactions on Biomedical Circuits and Systems, vol. 10, no. 4, pp. 912–919, Aug. 2016.
- C. Dimas, P. Tsampas, N. Ouzounoglou, and P. P. Sotiriadis, “Development of a modular 64-electrodes Electrical Impedance Tomography system,” in 2017 6th International Conference on Modern Circuits and Systems Technologies (MOCAST), 2017, pp. 1–4.